## Slide 1: System Dynamics and Vibrations
Prof. Gustavo Alonso
School of General Engineering Beihang University (BUAA)
Chapter 4: Applications of single degree-of-freedom systems

## Slide 2: Contents
Vibration measurement instruments
Acceleremeters / Seismometers

## Slide 3: Vibration measuring instruments
Used to measure:
  Displacements
  Accelerations
Normally these instruments consist of:
  A case containing a mass-damper-spring system
  A transducer measuring the displacement of the mass relative to the case
    it converts mechanical energy into electrical energy
  Mass: seismic mass
  Damping: viscous fluid

## Slide 4: Vibration measuring instruments
Absolute displacement of the mass: x(t)
Displacement of the case: y(t)
Displacementt of the mass relative to the case: z(t)

## Slide 5: Harmonic motion of the base
Equipment placed on a vibrating foundation
Vehicle traveling on a bumpy road
Engine mounted on an aircraft wing
...

## Slide 6: Harmonic motion of the base

## Slide 7: Harmonic motion of the base

## Slide 8: Vibration measuring instruments
y(t): vibration we want to know
z(t): vibration we measure

## Slide 9: Vibration measuring instruments
vibration we want to know
harmonic solution

## Slide 10: Vibration measuring instruments

## Slide 11: Vibration measuring instruments
measurement amplitude

## Slide 12: Vibration measuring instruments

## Slide 13: Vibration measuring instruments

## Slide 14: Contents
Vibration measurement instruments
Acceleremeters / Seismometers

## Slide 15: Accelerometers – high frequency instruments
If is small
then
is the acceleration of the case

## Slide 16: Accelerometers – high frequency instruments
If is small
then
is the acceleration of the case
the natural freqeuncy of the instrument is high relative to the frequency we want to measure
the measurement amplitude Z0 is proportional to the acceleration of the case (parabola)

## Slide 17: Accelerometer

## Slide 18: Accelerometers – high frequency instruments
Light damped accelerometers:
the natural frequency of lightly damped accelerometers must be appreciably larger than the frequency of the harmonic motion to be measured

## Slide 19: Accelerometers – high frequency instruments
Light damped accelerometers:
the natural frequency of lightly damped accelerometers must be appreciably larger than the frequency of the harmonic motion to be measured
 to increase the range of utility of the instrument, larger damping is necessary

## Slide 20: Accelerometers – high frequency instruments
 to increase the range of utility of the instrument, larger damping is necessary

## Slide 21: Accelerometers – high frequency instruments
Some considerations:
Accelerometers need calibration to measure x(t) from the static equilibrium of the seismic mass (effect of gravity)
More sophisticated accelerometers are used to measure vibrations in aircraft and missiles (in these cases the accelerometer may not be parallel to the gravitational force)  tilt table

## Slide 22: Accelerometers – high frequency instruments
The most commonly used accelerometers are the compression-type piezoelectric accelerometers
They consist of a mass resting on a piezoelectric ceramic crystal, such as quartz, barium titanate, or lead zirconium titanate, with the crystal acting both as spring and sensor
The accelerometers have a preload providing a compressive stress
exceeding the highest dynamic stress expected
Any acceleration increases or decreases the compressive stress in the piezoelectric element, thus generating an electric charge appearing at the accelerometer terminals
Piezoelectric accelerometers have negligible damping and they typically have a frequency range from 0 to 10,000 Hz (and beyond) and a natural frequency range from 30,000 to 50,000 Hz
They tend to be very light, weighing less than 20 g, and are relatively small, measuring less than 2 cm in diameter.

## Slide 23: Accelerometers – high frequency instruments

## Slide 24: Accelerometers – high frequency instruments
accelerometers
shaker or vibration table

## Slide 25: Seismometers – low frequency instruments

## Slide 26: Seismometers – low frequency instruments
If is large
then regardless the amount of damping
If we want to measure displacements, then we should make the natural frequency of the instrument very low relative to the frequency to be measured
 seismometer

## Slide 27: Seismometers – low frequency instruments
A seismometer is an instrument designed to measure ground displacements, such as those caused by earthquakes, or underground nuclear explosions
The requirement for a low natural frequency dictates that the spring be very soft and the mass relatively heavy, so that, in essence, the mass remains nearly stationary in inertial space while the case, being attached to the ground, moves relative to the mass.
Displacement-measuring instruments typically have a frequency range from 10 to 500 Hz and a natural frequency between 1 and 5 Hz.

## Slide 28: Seismometers – low frequency instruments
Because seismometers require a much larger mass than accelerometers and the relative motion of the mass in a seismometer is nearly equal in magnitude to the motion to be measured, seismometers are considerably larger in size than accelerometers.
In view of this, if the interest lies in displacements, it may prove more desirable to use an accelerometer to measure the acceleration of the case, and then integrate twice with respect to time to obtain the displacement.

## Slide 29: Arbitrary motion
So far we have considered the measurement of harmonic motion
In measuring more complicated motions, not only the amplitude but also the phase angle comes into play
There are two cases in which the accelerometer output is able to reproduce the motion y(t) without distortion:
  No damping: z = 0
  The phase angle is proportional to the frequency: z = 0.707

## Slide 30: Arbitrary motion
Any arbitrary motion can be regarded as a superposition of harmonic components
Hence, an accelerometer can be used for measuring arbitrary motions if the damping factor z is either equal to zero or equal to 0.707 ( )

## Slide 31: Exercise 1: design of seismometer
A seismometer having a natural frequency of 4 rad/s and z = 0.2
is attached to a structure that performs a harmonic motion.
If the difference between the maximum and the minimum recorded values is 8 mm, find the amplitude of motion of the vibrating structure when its frequency is 40 rad/s.

## Slide 32: Exercise 1: design of seismometer
A seismometer having a natural frequency of 4 rad/s and z = 0.2
is attached to a structure that performs a harmonic motion.
If the difference between the maximum and the minimum recorded values is 8 mm, find the amplitude of motion of the vibrating structure when its frequency is 40 rad/s.

## Slide 33: Exercise 1: design of seismometer
A seismometer having a natural frequency of 4 rad/s and z = 0.2
is attached to a structure that performs a harmonic motion.
If the difference between the maximum and the minimum recorded values is 8 mm, find the amplitude of motion of the vibrating structure when its frequency is 40 rad/s.

## Slide 34: Exercise 2: design of accelerometer
An accelerometer has a suspended mass of 0.01 kg with a damped natural frequency of vibration of 150 Hz.
When mounted on an engine undergoing an acceleration of 1g at an operating speed of 6000 rpm, the acceleration is recorded as 9.5 m/s2 by the instrument.
Find the damping constant and the spring stiffness of the accelerometer.

## Slide 35: Exercise 2: design of an accelerometer
An accelerometer has a suspended mass of 0.01 kg with a damped natural frequency of vibration of 150 Hz.
When mounted on an engine undergoing an acceleration of 1g at an operating speed of 6000 rpm, the acceleration is recorded as 9.5 m/s2 by the instrument.
Find the damping constant and the spring stiffness of the accelerometer.
ratio of displacements (case with respect to mass)
ratio of accelerations (case with respect to mass)

## Slide 36: Exercise 2: design of an accelerometer
An accelerometer has a suspended mass of 0.01 kg with a damped natural frequency of vibration of 150 Hz.
When mounted on an engine undergoing an acceleration of 1g at an operating speed of 6000 rpm, the acceleration is recorded as 9.5 m/s2 by the instrument.
Find the damping constant and the spring stiffness of the accelerometer.

## Slide 37: Exercise 2: design of an accelerometer
An accelerometer has a suspended mass of 0.01 kg with a damped natural frequency of vibration of 150 Hz.
When mounted on an engine undergoing an acceleration of 1g at an operating speed of 6000 rpm, the acceleration is recorded as 9.5 m/s2 by the instrument.
Find the damping constant and the spring stiffness of the accelerometer.

## Slide 38: Exercise 2: design of an accelerometer
An accelerometer has a suspended mass of 0.01 kg with a damped natural frequency of vibration of 150 Hz.
When mounted on an engine undergoing an acceleration of 1g at an operating speed of 6000 rpm, the acceleration is recorded as 9.5 m/s2 by the instrument.
Find the damping constant and the spring stiffness of the accelerometer.

## Slide 39: Exercise 2: design of an accelerometer
An accelerometer has a suspended mass of 0.01 kg with a damped natural frequency of vibration of 150 Hz.
When mounted on an engine undergoing an acceleration of 1g at an operating speed of 6000 rpm, the acceleration is recorded as 9.5 m/s2 by the instrument.
Find the damping constant and the spring stiffness of the accelerometer.